## Slide 1: BEST PRACTICES FOR COLLECTING WATER SAMPLES FOR ANALYSES
WILLIAM W. EFFIOK FIPAN
QSM TRAINING & CONSULTING LTD.
68 RANDLE AVENUE
SURULERE, LAGOS, NIGERIA

## Slide 2: OBJECTIVE OF TRAINING
TO OBTAIN CORRECT, AND RELIABLE RESULTS
NOTE:
Poor or wrong sampling always leads to false results.

## Slide 3: DEFINITION
SAMPLING. This is involvement of the task designed to select some part of a product/substance/material for a decided purpose.
SAMPLE. Sample is a part of a material collected according to a defined sampling procedure (SOP).
SAMPLING PLAN. A sampling plan describes the location, the number of units and quantity of material that should be collected, and associated acceptance criteria (Checklist).

## Slide 4: DEFINITION
SAMPLING PROCEDURE. The sampling procedure is the complete sampling operations performed on a defined material for a specific purpose (SOP, Precautions, Transport logistics, Delivery).
SAMPLING UNIT. A sampling unit is a discrete part of a consignment/location such as an individual package, drum, or container or yard tap or borehole (representative sample).

## Slide 5: WHAT TO PUT IN PLACE BEFORE SAMPLING
DEFINE THE PURPOSE FOR WHICH SAMPLE IS COLLECTED
IDENTIFY A LAB THAT WILL CARRY OUT THE ANALYSES
DISCUSS AND AGREE ON LOGISTICS FOR SAMPLING:-
This include:
A. who collect the sample
B. time sample should be collected
C. onsite tests required
D. preservatives and sample delivery time at the laboratory
E. sample size
F. sampling method

## Slide 6: DEVELOP A SAMPLE COLLECTION CHECKLIST
WATER TYPE: RIVER, STREAM OR BOREHOLE (PIPED AND TAP)
SAMPLING | FILL | COMMENT
DATE AND TIME |  | 
SITE DESCRIPTION |  | 
SAMPLING DEPTH/LOCATION |  | 
DISTANCE FROM REFUSE |  | 
SAMPLE VOLUME |  | 
WATER TEMPERATURE |  | 
TRANSPORT TEMPERATURE |  | 

## Slide 7: CHECKLIST CONT.
RIVER, STREAM OR BOREHOLE WATER
STORAGE | FILL | COMMENT
STORAGE TIME |  | 
STORAGE TEMPERATURE |  | 
SPECIAL OBSERVATIONS |  | 
SHIPMENT |  | 
DATE SAMPLE SENT |  | 
SHIPPING TEMPERATURE |  | 
DATE SAMPLE RECEIVED |  | 
CONDITION UPON RECEIPT |  | 
SPECIAL OBSERVATION |  | 

## Slide 8: SAMPLING MATERIAL CHECKLIST
IMPORTANT
MATERIAL | DESCRIPTION | TICK
SAMPLING CONTAINER |  | 
TOOLKIT |  | 
PRESERVATIVE |  | 
COOLING SYSTEM |  | 
POTABLE TESTING METERS |  | 
DOCUMENTATION MATERIALS |  | 

## Slide 9: QUICK GUIDE AND CONSIDERATIONS
DETERMINE WHETHER SAMPLE IS TO MEET REGULATORY REQUIREMENTS
IF YES, THIS WILL DETERMINE THE TEST METHODS TO USE
DETERMINE THE SCOPE OF THE PROJECT. WHAT IS THE END USE OF THE WATER?
THIS WILL DETERMINE THE TEST PARAMETERS
DISCUSS APPROPRIATE METHODS. THIS WILL DETERMINE THE SAMPLE SIZE AND VOLUME
IDENTIFY CONSTRAINTS AND HOW TO OVERCOME THEM.

## Slide 10: COLLECTION BOTTLES AND MATERIALS
BE PREPARED FOR SAMPLING. ICE PACKS AND OTHER PRESERVATIVE SHOULD BE AVAILABLE.
ANALYSES | BOTTLE TYPE | COMMENT
METALS | PLASTICS | SOME METALS MAY REACT WITH GLASS
ORGANICS AND PESTICIDES | GLASS | PLASTICS LEAKS ORGANICS
LIGHT SENSITIVE ANALYTES | AMBER | PROTECT FROM LIGHT
BACTERIAL | STERILE BOTTLE | AVOID CONTAMINATION
VOLATILE ORGANICS | GLASS | FILL AND LEAVE NO HEAD SPACE

## Slide 11: PRESERVATIVES AND HOLDING TIME
IMPLICATIONS
FACTOR | USE | COMMENT
SODIUM THIOSULPHATE | INHIBIT MICROBIAL GROWTH AND PREVENT CHEMICAL BREAKDOWN | COMMON AND EFFECTIVE PRESERVATIVE FOR WATER.
HYDROCHLORIC ACID | AS ABOVE. ADDED AT SITE | TO SUSTAIN PRESERVATION PROPERTY
30 HOUR HOLDING TIME | CLOSTRIDIUM AND ENTEROCOCCI | BACTERIA CAN SURVIVE LONGER STRESS PERIOD
6 HOUR HOLDING TIME | E. coli, COLIFORM | OPTIMAL FOR LIGHT CONTAMINATION
TEMP 4-6 DEGREES CELSIUS | INHIBIT MICROBIAL GROWTH AND BREAKDOWN OF CHEMICALS | MAINTAIN ALSO THROUGHOUT HOLDING TIME
PREFERRED COLLECTION TIME | LATE EVENING OR NIGHT | MORNING SAMPLE IF IT CAN ARRIVE AT LAB IN 6 HOUR
USE OF ICE | WET ICE OR ICE GEL | A MUST IN HOT CLIMATE

## Slide 12: SAMPLING TECHNIQUES
INITIAL CONSIDERATIONS
1. STATE WATER TYPE (Tapped well Water, Municipal water supply)
2. STATE TREATMENT STATUS (Treated, Not treated)
3. COLLECT REPRESENTATIVE SAMPLE (Run water for several minutes, avoid gooseneck)
Running water flush the system and get rid of transient contamination.
Before running water, remove any aerator from the spigot (tap) that may cause oxidation of metals and interfere with anaerobic growth.
Run tap for 2 to 3 minutes until pH, temperature and conductivity measurements for three samples taken in a row are consistent. THEN COLLECT SAMPLE.

## Slide 13: ORDER OF SAMPLING
SAMPLE SYSTEMATICALLY AS FOLLOWS:-
Start with samples for any field parameters (pH, temperature, conductivity)
Then move on to any light gases, such as volatile organics or methane, ethane and propane.
Next, collect any samples that do not require filtration or preservatives like metals, some inorganics and semi-volatile organics.
When testing for dissolved metals, you will need to field filter samples, and these varieties should be collected next.
Finally, collect samples for bacteria detection. Before sampling bacteria, turn the water off and disinfect spigot (Tap).

## Slide 14: NOTES ON BACTERIA SAMPLES
IF THE TAP FAUCET IS PLASTIC; use alcohol swab to disinfect
IF THE TAP HEAD IS METAL; use flame to disinfect
DO NOT COLLECT SAMPLE FROM GOOSENECK TAP; it is difficult to disinfect and thus not representative.
WEAR GLOVES TO PREVENT CONTAMINATION
USE STERILISED BOTTLES 250 ML
USE SEALED PRE-PRESERVATIVE BOTTLES
WHEN COLLECTING SAMPLE, HOLD CAP IN YOUR HAND. DO NOT LAY IT DOWN TO AVOID CONTAMINATION.

## Slide 15: SAMPLING TOOLKIT
ASSEMBLE A TOOLKIT:-
1. ONSITE TESTING METER
2. WRENCH TO DISMSNTLE AERATORS
SCREWDRIVER AND OTHER PLUMBING TOOLS
GLOVES
ALCOHOL SWAB
FLASHLIGHT

## Slide 16: SAMPLING POINTS
Where you collect the samples will depend on the objective of the analysis.
For instance, if you are collecting a sample to establish a baseline of water quality for a private well, you should gather the sample prior to any treatment devices.
It’s important to inspect for treatment equipment because many homeowners will not recognize a sediment filter as water treatment.

## Slide 17: SAMPLING POINTS CONT.
In most cases, collecting a sample from the kitchen sink is recommended, unless there is a specific water quality issue being experienced at a different tap, like a bathroom sink.
To determine if treatment equipment is functioning, you may need to collect "before" and "after" examples to get the best idea of how the equipment is operating.
To meet a particular regulation, where you obtained the sample is usually specified.

## Slide 18: DOCUMENTATION
THE SAMPLER MUST KEEP AN UP TO DATE FIELD NOTEBOOK
THE FIELD NOTEBOOK SHOULD CONTAIN RECORDS OF ALL FIELD TESTS AND PHYSICAL OBSERVATION INCLUDING WEATHER CONDITIONS
ALL SAMPLES MUST BE ACCOMPANIED WITH CUSTODY FORMS.
CUSTODY FORM SHOULD INDICATE DATE AND TIME SAMPLE WAS COLLECTED. OTHER INFORMATION SHOULD INCLUDE:
1. SAMPLING LOCATION
2. FIELD RESULTS AND OBSERVATIONS
3. ANALYSES REQUIRED
4. WHO DID THE SAMPLING
NOTE: SAMPLING TIME IS NECESSARY TO DETERMINE WHETHER THE SAMPLE IS WITHIN THE HOLDING TIME FOR THE ANALYTES.

## Slide 19: SAMPLING WASTE WATER
THE FOLLOWING INFORMATION SHOULD BE PROVIDED
1. NATURE OF WASTE WATER (PHARMACEUTICAL, BREWERY INDUSTRY, LIVESTOCK).
2. TREATED OR NOT TREATED
3. INTENDED USE OF WASTE WATER (DISCHARGE INTO BODY OF WATER, IRRIGATION, RECYCLE)
4. PURPOSE FOR WHICH SAMPLE IS COLLECTED
5. REGULATIONS CONCERNING THE WASTE WATER AND ITS INTENDED USE.

## Slide 20: UNDERSTANDING YOUR WASTE WATER
The most common issue for food and beverage manufacturers for example is biological oxygen demand, or BOD.
This is essentially organic carbon, but if you put too much of it down the drain, it causes a problem for the centralized treatment facility.
This is typically the largest cost, and it can account for 65-80% of wastewater management costs.
Other components include total suspended solids (TSS), nitrogen, phosphorus, fats, oils and greases (FOG).

## Slide 21: SAMPLING WASTE WATER
FOLLOW REGULATION FOR SPECIFIC WASTE WATER WHERE GIVEN
FOR ANAEROBIC BACTERIA COLLECT WATER TO FILL THE CONTAINER LEAVING NO HEAD SPACE
FOR ORGANICS AND METALS TREAT AS INDICATED FOR RIVER

## Slide 22: CONCLUSION
I WILL TAKE QUESTIONS NOW
THANK YOU.